## Slide 1
Block Diagram Representation of control systems and their manipulation
Block Diagram treatment for hydraulic position control
MM2DYN Dynamics: Control Lecture 3

## Slide 2
Lecture Objectives:
Demonstrate Block diagram manipulation
Demonstrate System modelling for a first order system
MMME2046 Dynamics and Control
Lecture 3

## Slide 3: Block Diagrams Revisited
Systems engineers represent the components of the system as a series of blocks:
Recap:
G(s)
Xi(s)
Xo(s)
The transfer function G(s) transforms the input Xi into the output X0
MMME2046 Dynamics and Control
Lecture 3

## Slide 4
G1Xi
Xi(s)
Xo(s)
G1(s)
G2G1Xi
G2(s)
Block Diagram Manipulation: The rules
a) Elements in Series
G2G1
Xo(s)
Xi(s)
Xo(s)
b) Elements in Parallel
+
_
+
G1(s)
G2(s)
Xi(s)
G3(s)
G1Xi
G2Xi
G3Xi
G1+G2 - G3
Xi(s)
Xo(s)
MMME2046 Dynamics and Control
Lecture 3

## Slide 5
c) Feedback (Closed loop) Transfer Function
Xi
Xo
Xo
+
_
G
Xi
H
Xi – HXo
d) Changing block positions:
+
_
Xo
G(s)
Xi
H(s)
G(Xi – HXo)
Xi – HXo
HXo
+
_
X
G
Y
Z
+
X
Y
_
Z
G
G
+
_
Xo
G
Xi
Xi – HXo
H
1/H
MMME2046 Dynamics and Control
Lecture 3

## Slide 6
d) Changing block positions
+
_
X
G
Y
Z
+
X
Y
_
Z
G
G
Check: Does this give the same result?
MMME2046 Dynamics and Control
Lecture 3

## Slide 7
e) Dealing with disturbances
R(s) is the input
C(s) is the output
D(s) is a disturbance
N(s) is a (user controlled) compensation
Procedure:
  Each of the inputs has its own independent transfer function. For R(s):
MMME2046 Dynamics and Control
Lecture 3

## Slide 8
e) Dealing with disturbances
R(s) is the input
C(s) is the output
D(s) is a disturbance
N(s) is a (user controlled) compensation
Procedure:
  For D(s):
MMME2046 Dynamics and Control
Lecture 3

## Slide 9
Xo
G1
G2
G3
H1
H2
Xi
+
_
+
_
Example: Reduce the block diagram and find the overall T.F.
Xo
Xi
+
_
+
_
G1
G2
G3
H2
i) Rearrange to avoid interlinking loops
H1 / G3
MMME2046 Dynamics and Control
Lecture 3

## Slide 10
ii) Eliminate the inner loop
Xo
Xi
+
_
G1
H1 / G3
iii) Reduce to a single block and simplify
Xi
Xo
Xi
Xo

## Slide 11
Position Control Systems
(case studies in 1st & 2nd order systems)
MM2DYN Dynamics: Control Lecture 5

## Slide 12
Lecture Objectives:
Introduce the differences between 1st and 2nd order systems
Analyse steady-state responses under step and ramp inputs
Analyse transient behaviour through the roots of the characteristic equations
MMME2046 Dynamics and Control
Lecture 3

## Slide 13: Video Interlude
Motherboard Assembly
  https://www.youtube.com/watch?v=ym64NFCWORY
Before we watch the video:
  Is the robot quicker than the employee?
  Was this robot customised for the application?
  What would happen if the robot overshoots?
MMME2046 Dynamics and Control
Lecture 3

## Slide 14
drain
drain
fluid in
spool valve
load
cylinder
piston
area, A
a
b
y
xo
xi
q
Xo
Xi
+
_
1/Ts
μ
Recap: Hydraulic Position Control System
It was shown that the transfer function is given by
with the block diagram (to be shown in this lecture)
1st order system
MMME2046 Dynamics and Control
Lecture 3

## Slide 15
Feedback link:

## Slide 16
Hydraulic Position Control System: Equations for the Model
Spool Valve
in the time domain
transfer function
(1)
Ram Piston
in the time domain
transfer function
Feedback Link
in the time domain
transfer function
(2)
(3)
MMME2046 Dynamics and Control
Lecture 3

## Slide 17
+
_
Xo
Xi
b/(a+b)
a/(a+b)
feedback link
Hydraulic Position Control System: Overall Transfer Function
(4)
From the block diagram
rearranging
First order system with time constant T and gain μ
K/As
spool valve and piston
MMME2046 Dynamics and Control
Lecture 3

## Slide 18
Xo
Xi
+
_
1/Ts
μ
Exercise: Show that the block diagram for a system governed by (4) can be drawn as
Xi
Xo
Hydraulic Position Control System: Control System Model
time constant
steady-state gain
MMME2046 Dynamics and Control
Lecture 3

## Slide 19: Exercise
From Equation 4:
First of all: recognise that gain is μ:
Xo
Xi
1/(1+Ts)
μ
MMME2046 Dynamics and Control
Lecture 3

## Slide 20: Exercise
From Equation 4:
Second: Unity feedback loop
Xo
Xi
G(s)
≡
Xo
Xi
MMME2046 Dynamics and Control
Lecture 3

## Slide 21: Exercise
From Equation 4:
Third:
Xo
Xi
Xo
Xi
MMME2046 Dynamics and Control
Lecture 3

## Slide 22: Time domain
Input is a unit step:
Output
Go to the table of Laplace transforms: No. 8
MMME2046 Dynamics and Control
Lecture 3

## Slide 23
Hydraulic Position Control System under Standard Inputs
i) step Input
t < 0
t ≥ 0
From the table of L.T.
(5)
The output in s-domain
(6)
In the time domain
(7)
speed of rise depends upon T
t
steady- state error
MMME2046 Dynamics and Control
Lecture 3

## Slide 24
Chart: 
| 0 | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 100
X(out) | 0 | 0.4424 | 0.78694 | 1.2642 | 1.7293 | 1.9634 | 1.9993 | 2 | 2
MMME2046 Dynamics and Control
Lecture 3

## Slide 25: Hydraulic Position Control System under Standard Inputs
We will return to this model in a later lecture to go through:
  Using the Final Value Theorem to calculate the steady state response and steady state error
  Examining the system’s response to a ramp input

## Slide 26: 2nd Order Control Systems
1st order systems are
  Reliable
  Non-oscillatory
  Slower than 2nd order
Hydraulics are slow and heavy
How do they do this?
  https://www.youtube.com/watch?v=U4y1grtRLDs

## Slide 27: 2nd Order Control Systems
Some examples – electro-mechanical position control
  Power steering
  n-degree of freedom robots
  …
Image courtesy of Bosch AG

## Slide 28: 2nd Order Control Systems
What is meant by “Second order systems”?
You will be familiar with 2nd order differential equations and their solutions:
  2 real roots (overdamped)
  1 root (critically damped)
  2 complex roots (underdamped)
MMME2046 Dynamics and Control
Lecture 3

## Slide 29
Example: Electro-Mechanical Position Control System
It will be shown that the transfer function may be written as
2nd order system
mass
viscous
damping
lead
screw
DC servo-
motor
servo-
amp
position
transducer
input
voltage
x (output)
Vi
fR
+
-
MMME2046 Dynamics and Control
Lecture 3

## Slide 30
2nd Order System
The transient responses under a step input for all three cases can be summarised
γ > 1
γ < 1
γ = 1
xo (t)
t
As can be seen, there is the danger of oscillation or overshooting
MMME2046 Dynamics and Control
Lecture 3

## Slide 31: Video Interlude
Highly automated VW Golf production line
  https://www.youtube.com/watch?v=3H1c_6_AxrQ
Questions:
  What would happen if the robot overshoots?
  Can speed/precision be improved?
  What controls the robots? Are they open or closed loop?
MMME2046 Dynamics and Control
Lecture 3

## Slide 32: Brilliant idea no. 1 - revisited
Centrifugal governor
  Patented 1788 by James Watt

## Slide 33: Method of operation for centrifugal governor
Video: https://www.youtube.com/watch?v=OG1AiaNTT6s
Drive from engine to governor
Engine
Control valve adjusts supply of steam to engine as linkage is moved by governor
Steam supply from boiler
As speed increases, flymasses rise and operate linkage
Angular velocity of governor shaft is proportional to engine rpm

## Slide 34: Brilliant idea no. 1 – centrifugal governor revisited
Speed control is achieved by negative feedback loop
  Too fast – steam input is reduced.
  Too slow – steam input is increased.
+
_
ω
Qin
K2
feedback (flymasses and valve)
K1/Js
Piston, flywheel and shaft
MMME2046 Dynamics and Control
Lecture 3

## Slide 35: What other information can we use?
Position – “are we there yet?”
Velocity – “can we go any faster?”
Integral – “how far have we come?”
MMME2046 Dynamics and Control
Lecture 3

## Slide 36: This will be covered in the control lectures next week.
Any questions?
P.S. There is an overview/revision lecture towards the end of the course.
MMME2046 Dynamics and Control
Lecture 3