## Slide 1: Seminar 4
Biot numbers, Fourier numbers and explicit equations

## Slide 2: Past exam question
(a) i) State what is meant by the terms Early Regime and Late Regime in transient heat transfer analysis. [2 marks]
An induction furnace at 500C contains a titanium rod of diameter 12 mm, initially at 20C, for a process known as annealing.
  ii) Show, by using the Biot number, that a lumped capacity analysis is applicable. [3 marks]
iii) Use the lumped capacity method to find the time for the core of the rod to reach 90% of the furnace temperature given an overall heat transfer coefficient of 200 W/m2K at the surface. [5 marks]
(Data: Assume the lumped capacity formula, /0=e-(hA/Vc)t. Use the density, conductivity and specific heat capacity of titanium, 5,000 kg/m3, 22 W/mK and 500 J/kgK.)

## Slide 3: Solutions
i) The Early Regime describes that part of transient heat transfer in which the material receiving the heat has not had time to respond to the heat wave impinging on it.
The Late Regime is that part during which the whole body of the material has made an initial reaction to the heat wave, and the whole body is in a process of heat transience.
The former term refers to situations in which thermal resistance transferring heat to the body is low relative to that inside the body (i.e. the body is slow to respond to the heat front), and the second term refers to situations in which the thermal resistance of heat transfer to the body is greater than that inside the body (i.e. the body responds quickly to the heat front).
The Fourier number compares the duration of transient heat transfer thus far (t) to the time for a heat front to diffuse into a length equivalent to the characteristic length of the body, L=V/A – volume/surface area. It is a dimensionless time.  is the thermal diffusivity, k/ρc.
ii) Bi = hV/kA = 2000.0122/2240.012 = 0.027; since Bi<<1, the lumped capacity analysis is valid.
iii) t = ln(θ/θ0)(-ρVc/hA) = ln (48/480)(-5,000 0.0122500/42000.012) = 86.3 s.

## Slide 4: Nodal analysis
A 1-D numerical solution is to be used to calculate how long it takes for the ground to heat up in the summer, assuming that it reaches a uniform temperature throughout to a depth of 5m during the winter and that the ambient conditions change suddenly from isothermal to a heat transfer coefficient of h W/m2K to the air at 20C.
i) Draw a schematic diagram, showing 5 nodes distributed in the depth of the ground, and determine the nodal equation for the surface node and a typical interior node. Collect terms to express your formulae in terms of the Fourier and Biot number. [5 marks]
ii) State what the condition for numerical stability is from these two node formulae, and find the time step for stability. [5 marks]
(Data: Assume for the ground that k = 1.5 W/mK, the heat transfer coefficient at the surface is 15 W/m2K, soil density is 1,500 kg/m3, soil specific heat capacity is 1.84 kJ/kgK, and the nodal distance is 1m. State your answer to the nearest whole hour.)

## Slide 5: Draw a schematic diagram, showing 5 nodes distributed in the depth of the ground, and determine the nodal equation for the surface node and a typical interior node. Collect terms to express your formulae in terms of the Fourier and Biot number. [5 marks]
For node 1, the energy equation:
And thus,
And similarly, for the typical body node (2-5)
1
5
5
2
3
4

## Slide 6: State what the condition for numerical stability is from these two node formulae, and find the time step for stability. [5 marks]
The condition for stability is that none of the coefficients of the nodal equations should be negative. This requires from the surface node that 1>2Fo(1+Bi), and for the interior node that 1>2Fo. Clearly, the former is the limiting factor, having the larger right hand side. In this case,
Bi = hL/k = 151/1.5 = 10,
 = k/c = 1.5/15001840 = 5.4310-7 m2/s
Fo = 5.4310-7t/1 = 5.4310-7t/1.252
For the condition to be satisfied:
1>25.4310-7t(1+10)
t<130,797 s or 36 hours.