## Slide 1
Combustion
Content
2.1 1st Law of thermodynamics applied to combustion
enthalpies of reaction, flame temperatures
2.2 Enthalpy and Entropy in Combustion Reactions
Absolute Entropy, Enthalpy of Formation and Hess’ Law
2.3 Chemical equilibrium in combusting systems
Application of 2nd Law of Thermodynamics
Dissociation in reacting systems and the Equilibrium Constant
Revision notes on combustion reactions on Moodle.

## Slide 2: Combustion – Lecture 1
Learning outcomes:
Understand how to apply 1st Law of thermodynamics (SFEE) to combustion using enthalpies of reaction
Understand how to calculate a flame temperature.
Understand how to use tables of molar enthalpy in combustion calculations.
Understand concepts of : Absolute Entropy, Enthalpy of Formation and Hess’s Law

## Slide 3
Combustion
= Molar enthalpy of combustion.
It’s a negative number.
Q + W = HP – HR
If TR = Tp = T0 25C then:

## Slide 4
Combustion
Physical form of reactants and products is important, example benzene from the tables:
of C6H6 vapour = -3 169 540 kJ/kmol water as vapour in products
of C6H6 liquid = -3 135 740 kJ/kmol water as vapour in products
of C6H6 vapour = -3 301 510 kJ/kmol water as liquid in products
Calorific value =
Higher (or gross) calorific value (HCV) - water as a liquid in products
Lower (or net) calorific value (LCV) - water as a vapour in products
Notation:
Wavy line is molar
Lower case is specific
Subscript 0 is standard state
Negative, - is out of system

## Slide 5: Of vapour and liquid
What we see here is the reaction energy of benzene with water as vapour.
If the benzene starts as liquid, then first the energy for evaporation hfg of benzene has to be taken off, 33,800 kJ/kmol, therefore 3,135,740 kJ/kg
Further to this, if the water vapour is condensed for useful heat recovery, then there is extra energy release of the water hfg. In the tables hfg for water is 2441.8 kJ/kg at 25C, i.e. 43,952.4 kJ/kmol. Alternatively, the value here is stated on p.21 of tables with benzene and octane.
For C6H6 there are 3 moles of water per mole of fuel, so difference due to hfg on the combustion reaction will be 343990 kJ per mole of fuel;
So with water as liquid instead of vapour from the reaction energy above, should have:
-3,169,540 kJ -343990 kJ = 3,330,510 kJ/kmol of fuel

## Slide 6
Combustion
Reactants and products at different temperatures
Q + W = HP – HR
Q + W = (HP - HP0) - (HR - HR0) + (HP0 - HR0)
mf ho combustion enthalpy

## Slide 7
For perfect gases, use:
Use mean cp over temperature range.
Note for water close to saturation and when there is a phase change use enthalpies from steam tables.
Combustion

## Slide 8
Sample of cp from tables – varying with temperature

## Slide 9
Combustion
Adiabatic Flame Temperature
Maximum possible temperature in a flame
Q + W = (HP - HP0) - (HR - HR0) + (HP0 - HR0) (if initial temp = 25 ºC)

## Slide 10
Combustion
2.1
Example - Calculation of Adiabatic Flame Temperature
Combustion of stoichiometric mixture of ethane (C2H6) and air from an initial temperature for the reactants of 25°C. h0 = -47 595 kJ/kg for ethane (water as vapour in combustion products).
C2H6 + aO2 + bN2 = 2CO2 + 3H2O + bN2
From atom balance:
Therefore: b = 3.76 x 3.5 = 13.16
Assume a unit quantity (ie 1 kg) of fuel, and hence determine masses per kg of fuel.
Reactants kmol Mass kg Mass/kg of fuel (mi)
C2H6 1 30 30 1
Products
Carbon dioxide 2 44 88 2.933
Water 3 18 54 1.8
Nitrogen 13.16 28 368.5 12.28

## Slide 11
Combustion
Guess a flame temperature to find a temperature to look up cp
2.1
Guess a flame temperature of 1700°C, determine mean specific heat capacities for products at mean temperature (1700+25)/2 = 863°C (say 1150 K).
Mean cp @ 1150 K CO2 = 1.27 kJ/kg K
(p 17 Rogers & Mayhew Tables) H2O = 2.392 "
N2 = 1.196 "
From equation for adiabatic flame temperature with reactants at 25°C:
Taf = 2120°C
With this improved estimation for Taf determine new mean cp.

## Slide 12
Combustion
Guess a flame temperature to find a temperature to look up cp
2.1
With this improved estimation for Taf determine new mean cp.
Mean temperature is (2120 + 25)/2 = 1073°C (1346 K)
say 1350 K
Mean cp @ 1350 K CO2 = 1.306 kJ/kg K
H2O = 2.521
N2 = 1.226
= 23.42 kJ/K
Taf = 2057°C
Actual flame temperature is always lower – due to heat transfer from the flame and dissociation

## Slide 13
C2H6 + 3.5 02 + 13.16 N2  2CO2 + 3H2O + 13.16 N2
From SFEE, for adiabatic combustion:
(Hp - HP0) - (HR - HR0) + H0 = 0
Express enthalpies in terms of molar enthalpies and numbers of moles,
If reactants are at 25°C, HR - HR0 = 0
Then
ni = number of moles of products per mole of fuel
for C2H6 = -1427860 kJ/kmol
at 25C, = 0 by definition (see Tables)
Combustion
Use of Molar Enthalpy - Tables p 18-20
Work directly from combustion equation – no need to convert to mass

## Slide 14
State enthalpy from tables – zero at 25C, 298.15K

## Slide 15
Therefore, choose a flame temperature to satisfy equation:
Use enthalpy values from pages 18 and 19 of Tables.
If T = 2200 K, then LHS of equation = 1290210 kJ
What is molar enthalpy of each product at 2200 K ?
If T = 2400 K, then LHS of equation = 1442159 kJ
By interpolation when T = 2381 K, LHS = 1427860 kJ
Therefore: Flame Temp = 2108°C
(The difference between these results illustrates the error resulting from the use of a mean cp. Variation in cp is not linear, especially over large temperature differences, hence this 2.5% error in temperature rise.)
Another example with preheated air is in the notes.
Combustion

## Slide 16
Combustion
More about Enthalpy and Entropy in Combustion
Third Law of Thermodynamics – absolute entropy
Entropy of all substances (elements and compounds) is zero at 0 K.
Entropies given in Tables p18-20 at 1 bar.
For gases at other pressures use:

## Slide 17
State entropy from tables – zero at 0K, -273.15K
Convenient reference temperature defined for enthalpy based on typical atmospheric conditions for combustion
Entropy zero point is a fact of nature

## Slide 18
Example on entropy at pressure and temperature
Although enthalpy doesn’t change significantly with pressure, entropy does
Find the absolute entropy of 1 kg of methane vapour at 400 K, 12 bar
S12 bar - S1 bar = -R loge 12
= -1.291 kJ/kg K
from tables, of methane at 400 K is 197.25 kJ/kmolK, therefore s (specific, per kg) of methane at 400 K is 12.33 kJ/kgK
s of 1 kg of methane at 400 K, 12 bar = 12.33 – 1.291 = 11.037 kJ/K

## Slide 19
Combustion
More about Enthalpy and Entropy in Combustion
Enthalpy of Formation – Hess’s Law
Allow for enthalpy changes in reactions using enthalpy of combustion. (need to know reaction enthalpy for each reaction) - we’ve just done this!
Use enthalpy of formation to give enthalpies of reactants and products.
Enthalpy of formation of elements in their standard state (i.e. some elements are standard as diatomic molecules) is defined as being zero at 25C, 1 bar.

## Slide 20
Combustion
Elements C, O2, H2
H
Reactants CxHy, O2
Products CO2, H2O
Hf0 reactants
Hf0 products
H0 reaction
Hess’s Law: H0 = Hf0 reactants – Hf0 products
2.2

## Slide 21
Combustion
Enthalpy
Enthalpy of formation of compound from it’s elements at 25C, 1 bar.
Change in enthalpy of compound to bring it to actual T and P.
= cp T for gases.
Note: enthalpy of gases does not change significantly with pressure.
2.2

## Slide 22
Selection of species showing formation enthalpy, hf0
~
Some are positive, some are negative…. What does it mean?
If in doubt look at CO2 being formed from C and O2 and think which way energy goes from the reactants.

## Slide 23
Combustion
Two methods to use SFEE for combustion:
2.2
Use enthalpy of formation
Enthalpy of reaction is included in enthalpy change
Use enthalpy of reaction

## Slide 24
Combustion
Example
Calculate gross calorific value of methane using enthalpies of formation
CH4 + 2O2  CO2 + 2H2O (liquid)
For CV calculation, reactants and products are at 25C, 1 bar
2.2
Remember enthalpy of combustion is heat absorbed when 1 mol is completely burned in oxygen
From 1st Law (SFEE)
Calorific value Qcv is the heat released when reactants and products start and end up at the 25ºC, 1 bar.
=(-74870 + 0 ) + 2 ( 0 + 0 ) as temperature is 25ºC
for oxygen (element)
= -74870 kJ/kmol

## Slide 25
Combustion
2.2
= (-393520 +0 ) + 2 (-285820 + 0 ) as temperature is 25ºC
= -965160 kJ/kmol
Qcv = -965160 - (-74870)
Qcv = -890290 kJ/kmol
Molec wt for methane is 16 kg/kmol. So:
Qcv = -55.64 MJ/kg this is negative as the heat leaves the system.

## Slide 26: Hydrogen - not in notes
2 kmol H2 and 1 kmol O2 react to give 2 kmol of H2O.
Reactants at 25C (298K) Products at 327C (600K)
SFEE: Q + W = HP– HR
Calculate heat released (Q) during reaction. (W = 0)
Use molar enthalpy
and mean specific heat capacity methods and compare answer.
Use data from tables provided for: , , and
(assume water vapour is perfect gas)Note: T0 = 25C (298K)

## Slide 27: Use molar enthalpy
2 kmol H2 and 1 kmol O2 react to give 2 kmol of H2O.
Reactants at 25C (298K) Products at 327C (600K)
Use molar enthalpy
Enthalpy of formation of reactants = 0 as they are both elements.
For reactants as they are at 25C (T0)
Number of moles of product = 2. Look up and for water from tables.
Q = 2 [-241830 + (10498 – 0)] = - 462664 kJ
Mass of products is 2 x 18 = 36kg.
So specific energy release is – 462664/36 = -1285 kJ/kg of water produced

## Slide 28: Use specific heat capacity and enthalpy of reaction
2 kmol H2 and 1 kmol O2 react to give 2 kmol of H2O.
Reactants at 25C (298K) Products at 327C (600K)
Use mean specific heat capacity methods and compare answer.
For reactants enthalpy is zero as they are at 25C (T0)
Mean product temperature is (298+600)/2 = 449K. Look up at 450K,1.926 kJ/kgK
Number of moles of product = 2, = 18 kg/kmol. So mass of product = 36 kg
Look up for water vapour from tables.
Q = 361.926 (600 – 298) + 2 (-241830) = - 462721 kJ.
(very close to 462664)
Mass of products is 2 x 18 = 36kg.
So specific energy release is – 462721/36 = -1285 kJ/kg of water produced

## Slide 29: Combustion – lecture 2
Learning outcomes
Understand chemical equilibrium in combustion reactions by applying 2nd Law of Thermodynamics (entropy increases when reactions take place) S increases for a reaction to happen
Understand what Gibbs Function is and its significance in determining chemical equilibrium, G=H-TS
Understand how to calculate the composition of a combustion reaction at equilibrium.
Understand the Equilibrium Constant and how it is calculated, K  equilibrium constant, derived from partial pressures – related to G
2.3

## Slide 30
Combustion
Chemical Equilibrium (Dissociation of Products)
At equilibrium there is no tendency for spontaneous change in a system:
Thermal Equilibrium – no temperature differences
Mechanical Equilibrium – no driving forces
Chemical Equilibrium - no driving changes in composition
Thermodynamic Equilibrium – everything is in equilibrium (no energy transfers)
2.3
p1
p2
p1=p2

## Slide 31
Combustion
CO
CO2
CO
CO
CO2
CO2
CO2
O2
O2
O2
O2
Chemical Reactions
Chemical reactions go in both directons.
CO + ½O2 CO2
Final composition depends on chemical equilibrium when driving forces in each direction are equal.
CO + ½ O2  (1-a)CO2 + aCO + ½ aO2
Equilibrium composition (value of a) can be found by considering entropy changes and 2nd Law of Thermodynamics.
2.3

## Slide 32
Entropy generation rate
At steady state:
Combustion
2.3

## Slide 33
Combustion
Adiabatic Reaction
Reaction proceeds until entropy is a maximum.
Equilibrium state is at maximum entropy.
Sgen
100%
Reactants
Equilibrium
composition
100%
Products
dS>0
dS = 0
dS<0
impossible
2.3

## Slide 34
Combustion
Chemical Reaction at specified temperature and pressure:
From the 1st Law
-dQ + dW = dU (NFEE) but dW = -pdV
So -dQ -pdV = dU
From 2nd Law:
dSgen = dSsys + dSsurr  0 (dSsurr = dQ/T)
dSgen = dSsys + dQ/T  0
TdSsys  -dQ
Substitute for dQ in 1st Law expression:
(dU + pdV) - TdSsys  0 → (H – TS)  0 (2)
Combustion Chamber
(system) (T,P)
At constant temperature and pressure
2.3

## Slide 35
Combustion
Chemical Reaction at constant temperature and pressure:
Now define a new quantity Gibbs Function G = H – TS
(also known as free energy or chemical potential)
To obey the second law of thermodynamics it is found that (derivation in notes):
dG(T,p)  0
Equilibrium state is at minimum Gibbs function
2.3

## Slide 36
Combustion
G(T,p)
100%
Reactants
Equilibrium
composition
100%
Products
dG<0
dG = 0
dG>0
impossible
So chemical reactions proceed until the Gibbs function is a minimum to obey 2nd Law.
2.3
dG(T,p)  0
Equilibrium state is at minimum Gibbs function

## Slide 37
Combustion
Equilibrium composition – use minimum Gibbs function approach
Chemical reaction aA + bB  cC + dD
Reaction proceeds a little dnA A + dnB B  dnC C + dnd D
Equilibrium is reached when dG(T,p) = 0
dnA = - a  is small reaction progressing a small amount
dnB = - b
dnC = + c
dnD = + d
all at T,p
2.3

## Slide 38
Combustion
for perfect gases
Substitute into
See notes for derivation of:
where
2.3

## Slide 39
Combustion
2.3
Equilibrium constant is defined as:

## Slide 40
Combustion
K does not have to be found experimentally – it can be found from Gibbs Function.
Note that in Rogers and Mayhew Tables, Gibbs function is expressed with enthalpy taken as zero at 25 deg C for all substances. - Enthalpy must be expressed in terms of enthalpy of formation to calculate G
aA + bB  cC + dD
2.3

## Slide 41
The Plimsoll line saves lives!

## Slide 42
Combustion
2.3
can also be written in terms of mole fractions.
Given mole fraction

## Slide 43
Combustion
2.3
Equilibrium constant is defined as:
a, b, c, d are the powers which are the mole number of each of the species in the completed stoichiometric reaction equation. The actual mole proportions at equilibrium are xa etc.

## Slide 45: Combustion – Lecture 3
Learning outcomes
Understand the properties of the Equilibrium Constant and how to use it.

## Slide 46
Combustion
K applies only to mixtures of perfect gases.
K is DEPENDENT upon temperature
K is INDEPENDENT of pressure. G(T) is evaluated at standard pressure of 1 bar, so K is independent of pressure of mixture. BUT……….
Total pressure of the mixture of gases affects the composition.
Presence of gases which do not take part in the reaction does not affect K, but does affect equilibrium composition, by affecting partial pressures.
If K is large the reaction will be more towards the products side and vice versa. aA + bB  cC + dD
K indicates the equilibrium composition but gives no indication as to how fast equilibrium is reached. The rate can only be determined from chemical kinetics theory.
2.3

## Slide 47
Combustion
When is Dissociation important?
If K is very large the composition will tend towards the products side.
If K is very small the composition will tend towards the reactants side.
Generally if K > 1000 (ie loge K >7) then the reaction may be assumed to have gone to completion for the purposes of calculating temperatures and enthalpies in the reactions. (If K is = 1000 then this implies that the partial pressure, and hence mole fraction, of the products is 1000 times that of the reactants at equilibrium)
Similarly if K < 0.001 (ie loge K < -7) then the reaction may be assumed not to have taken place.
Examples:
See p 21 in Rogers and Mayhew tables for values of K.
Dissociation of H2O into H2 and O2 is only important when T > 2000 K.
Dissociation of O2 into atomic O is only important when T > 2600 K
Dissociation of N2 into atomic N is only important when T > 5000 K
Dissociation of CO2 into CO and O2 is only important when T > 1800 K
Reaction of N2 and O2 to form NO is only important when T > 1000 K
Reaction of H2O and CO to form H2 and CO2 is only important when T > 400 K
(but CO will not usually be present if there is plenty of O2 about)
2.3

## Slide 48
Combustion
Examples
See p 21 in Rogers and Mayhew tables for values of K.
Dissociation of H2O into H2 and O2 is only important when T > 2000 K.
Dissociation of O2 into atomic O is only important when T > 2600 K
Dissociation of N2 into atomic N is only important when T > 5000 K
Dissociation of CO2 into CO and O2 is only important when T > 1800 K
Reaction of N2 and O2 to form NO is only important when T > 1000 K
Reaction of H2O and CO to form H2 and CO2 is only important when T > 400 K
(but CO will not usually be present if there is plenty of O2 about)
2.3

## Slide 49
Combustion
Competing reactions: solve reactions simultaneously.
Examples:
(i) H2 + ½O2  H2O Reaction of H2 and O2 to form water
A B C
a = 1
b = 0.5
c = 1
(ii) ½O2 + ½N2  NO
A B C
a = 0.5
b = 0.5
c = 1
(iv) Alternatively for (i) we could write:
(iii) ½O2  O 2H2 + O2  2H2O
A C A B C
a = 0.5 a = 2
c = 1 b = 1
c = 2

## Slide 50
Combustion
Form of stoichiometric equation is important
(i) ½O2 + ½N2  NO
A B C
a = 0.5
b = 0.5
c = 1
OR
(ii) O2 + N2  2NO
A B C
a = 1
b = 1
c = 2
In tables K is written for stoichiometric equation (i) So you must use that equation in
determining equilibrium composition.

## Slide 51
Combustion
For the reaction below calculate the mole fraction of nitric oxide when oxygen and nitrogen react at 1800 K and 1 bar
Write the reaction as
What would the mole fraction of NO be if pressure were 10 bar?

## Slide 52
Combustion
For the reaction below calculate the mole fraction of nitric oxide when oxygen and nitrogen react at 1800 K and 1 bar
Write the reaction as:
at 1800 K, stoichiometric coefficients are: a = ½, b = ½, c = 1
Total number of moles at equilibrium is:
, K = 0.0109 ()
Substitute in mole fraction equation for K.
, so concentration of NO at equilibrium is 0.54%
At 10 bar, there will be no change to the equilibrium composition as the total pressure term is 1.

## Slide 53
Combustion
Example 2 Calculation of
Calculate for the reaction at 2000 K
In general:
-478110 at 2000 K
-447800 at 2000 K
as O2 and N2 are elements, hf0 = 0, so can use values of directly from tables without having to use enthalpy of formation
This agrees with value from Tables (but change sign because reaction has been written the other way round)

## Slide 54
Example 3
The products from the combustion of a stoichiometric mixture of CO and 02 are at a pressure of 1 bar and a certain temperature. The products analysis shows that 35% of each kmol of C02 is dissociated. Determine the equilibrium constant for this temperature, and then find the percentage dissociation when the products are at the same temperature but compressed to 10 bar.
The combustion equation for the reaction to products in equilibrium is:
Where is the fraction of CO2 dissociated.
At 1 bar the products consist of:
0.65 kmol CO2 + 0.35 kmol CO + 0.175 kmol O2
The total amount of substance of products is 1.175 kmol, and the partial pressures of the constituents in bar are therefore:

## Slide 55
Calculate Adiabatic Flame Temperature – allowing for chemical equilibrium for combustion at constant pressure
Is Hp = Hr+mh0?